## Slide 1: Digital radiography

## Slide 2: What is it?
It is recording a map of x-ray transmissions through the patient into a digital file
Uses conventional x-ray machines
Viewing images as a digital file
NOT running radiographs through a scanning device
NOT taking radiographs with a digital camera

## Slide 3
Digital images are made from pixels
More pixels equals better detail
More pixels equals bigger file size
Image files are in DICOM format

## Slide 4: DICOM
Digital imaging and communications in medicine
System of software standards
Allows different digital imaging software to understand each other
Originally each vendor had own format
File contains

## Slide 5: Digital imaging terms
CR
DDR

## Slide 6: Computed radiography
Reusable, sensitive imaging plate within a cassette
Cassette then loaded into a reader

## Slide 7: Computed radiography
Advantages
Disadvantages

## Slide 8: Direct digital radiography
Direct capture system
No cassette
3 types

## Slide 9: Charged coupled device
Image quality is a function of light collection, lens and number of pixels within camera chip
X-ray through
2 types of scintillators
  Cesium Iodide (CSI) – better images $$$
  Gadolinium Oxide (GADOX)
CCD detectors quite large not practical for LA

## Slide 10: Flat panel
Indirect
  X-rays
Direct
  X-ray

## Slide 11: Flat panel
In theory expect direct to have better image quality since no screen but really no detectable difference
No cassettes, camera or lens
Immediate viewing
Panel can be portable
When purchase you buy new table and machine

## Slide 12: Film vs CR vs DR
Differences
  No cassette in DR
  No processing in DR
  No reloading of a cassette in DDR
Similarities
  Positioning
  Measure
  Technique
  Enter data

## Slide 13: Which to buy?
Personnel preference and $$$$
Convenience and quality of flat panel
Hard to keep up with technology

## Slide 14: Spatial resolution
The minimum size of an object that can be seen within an image

## Slide 15: Why bother
Detail not as good so what’s the big deal??????
  No hard copy
  Exposure latitude
  Contrast optimization
  Post processing
  Consultation
  Professional image

## Slide 16: No hard copy
No darkroom
  Chemicals
  Space
Can review image all over clinic
Can manipulate image
No deterioration of image
Can’t lose/misfile images

## Slide 17: Exposure latitude
Extent to which a film/image plate of flat panel can be over/under exposed and still achieve an acceptable image

## Slide 18: Exposure latitude
Doesn’t mean that over/under exposure is not a problem
Overexposure
  In film the image becomes darker
  In digital this doesn’t happen because the computer algorithm compensates
  “creep”

## Slide 19: Contrast optimization
Dark regions made lighter and light regions made darker
Creates a smoother x-ray with optimized contrast
Notes: Left is a typical good analog image – areas of under and over exposure
Right is a digital image – smoother rad with optimized contrast

## Slide 20: Contrast optimization
Happens by the programming of the software
When an image is captured it becomes a histogram
Histogram then evaluated for contrast/density based on an algorithm
Software has baselines (look up tables LUT) based on what examination is performed

## Slide 21: Post processing
Ability to ZOOM!!!!!!
Can detect very subtle changes now
Can alter contrast and blackness after acquisition

## Slide 22: Consulting
Can send images and receive a consult in a short amount of time

## Slide 23: Misconceptions
Exposure factors are decreased
  Not true
  Very comparable to analog system
  Remember creep
    Images don’t get darker as exposure factors are increased
  Some systems have exposure index option
    Number that is displayed
    Shows exposure used vs exposure needed

## Slide 24: Misconceptions
Artifacts are eliminated
  Dark room
  Improper exposure
  Position
  Insufficient views
  Poor radiation safety practices

## Slide 25: Monitor
Can be the weakest link to the system
Image is only as good as the weakest link
Recommended
  2 high quality monitors for image review
  Monitor for clients doesn’t have to be as high
Don’t need a medical grade necessarily
  1920 x 1200 resolution is recommended

## Slide 26: Storage
Remember computers fail
Store data in more than 1 place
Interchangeable external hard drives