## Slide 1: The Production of X-Rays
Amy Crane, DVM

## Slide 2: In this Lecture
What x-rays are
The components of an x-ray tube
How x-rays are produced
Understand the line focus principle
Understand why an anode rotates
Understand Heel Effect
Understand how x-ray generators work
Understand what line voltage compensation is and why it is important

## Slide 3
Ah, radiation physics! It is not that bad…..really.
Think of this as building blocks. Have to start somewhere
Same goes for radiology. Without learning the physics, you can still take radiographs – but don’t know how to fix one if it comes out crummy.

## Slide 4: X-rays: The core of radiology
Definition: x-rays are a form of electromagnetic radiation traveling through space as a combination of electric and magnetic fields. Radio waves, television waves, microwaves, and light are other forms of electromagnetic radiation. X-rays have a shorter wavelength and higher frequency than visible light.

## Slide 5
X-rays have a number of useful physical characteristics that allow us to utilize them for our benefit

## Slide 6
X-rays can penetrate matter
–

## Slide 7
X-rays also interact with matter, which causes biological alterations (ionization) at the molecular level. This of course is not always beneficial as x-rays can be damaging.
More on this later

## Slide 8
X-rays cause certain materials to fluoresce

## Slide 9
When interacting with matter, x-rays follow many of the same physical principles as light

## Slide 10: Such as…….(deep breath)
X-rays act like waves when traveling through space
X-rays act like particles when interacting with matter
X-rays travel in straight lines.
X-rays diverge from a point source

## Slide 11
X-rays obey the inverse square law.
X-rays are not affected by magnetic fields.
X-rays travel at the speed of light.

## Slide 12: Roentgen’s 12 laws of x-rays
1. Are highly penetrating invisible rays that are a form of electromagnetic
radiation
2. Are electrically neutral and therefore not affected by either electric or
magnetic fields
3. Can be produced over a wide variety of energies and wavelengths
4. Release very small amounts of heat upon passing through matter
5. Travel in straight lines
6. Travel at the speed of light
7. Can ionize matter
8. Cause fluorescence of certain crystals
9. Cannot be focused by a lens
10. Affect photographic film
11. Produce chemical and biological changes in matter through ionization and excitation
12. Produce secondary and scatter radiation

## Slide 13: Basic Components of an x-ray tube:
Air evacuated glass envelope
Cathode
Anode
Others

## Slide 14: 5 things required for x-ray production
source of electrons
way to accelerate electrons
path free of obstacles for electrons to pass thru
target for electrons to interact with to release energy as x-ray
tube for vacuum environment

## Slide 15: Cathode first
filament is made of tungsten
filament is heated to produce electron source
# of electrons released dependant on heat

## Slide 16: Cathode first
After electrons released from filament they must be accelerated
mA and KVp are the 2 major settings on the x-ray machine

## Slide 17: Cathode first
Filament is housed within a focusing cup to direct electrodes across to anode

## Slide 18: At the anode: Turning electrons into x-rays
The statement “x-rays are formed” won’t quite cut it. Here is a little more on that process

## Slide 19: At the anode: Turning electrons into x-rays
When the electrons from the cathode hit the target on the anode the energy from the electrons changing directions is released as

## Slide 20: At the anode
target on the anode is usually tungsten
heat dissipation is extremely important
-copper base draw heat from target
-oil around glass tube helps also

## Slide 21: At the Anode
electrons from cathode have a collision with the target on the anode what is produced and at what percentages???????

## Slide 22: how this relates to an x-ray machine
mA control –
kVp –
Higher kVp = faster travel and greater kinetic energy.
99% of the energy is released as heat and only 1% as x-rays.
spectrum of energies released ranging from 0- chosen kVp. most of the x-ray beam will be ⅓ of the peak kVp.

## Slide 23: 2 types of Anodes
Stationary
rotating

## Slide 24: Stationary anode
used in some portable units and dental units
if they get to hot at the focal point the anode will become pitted
These units have light to warn you and tell you when ready

## Slide 25: The Rotating Anode: The sweet song of an x-ray machine
If you have ever taken an x-ray, you know that you are supposed to push a button half way and wait while something in the machine starts to spin and hum.
Why rotating?

## Slide 26: The Rotating Anode: The sweet song of an x-ray machine
If it did not spin

## Slide 27: The Rotating Anode: The sweet song of an x-ray machine
Heat dissipation also has two other effects besides prolonging the life of the anode

## Slide 28: Focal spots and the Line Focus Principle
focal spot is where the electrons collide on anode
The size of the focal spot influences the detail of the image

## Slide 29: Focal spots and the Line Focus Principle
Fortunately, there are solutions to this heat problem

## Slide 30: Line Focus Principle
Line Focus Principle
–The anode is angled toward the cathode, this allows us to use a larger actual focal spot while reducing the size of the effective focal spot

## Slide 31: Line focus principle
Actual focal spot
• Effective focal spot

## Slide 32: Line Focus Principle
Best described by the angle of the anode
  The smaller the angle of the anode the smaller the effective focal spot
  12 degree target angle most common because it is the minimum a 14 x 17 cassette

## Slide 33: Focal spots and the line Focus Principle
SOOOOO the definition of the line focus principle is that the angling of the anode results in the effective focal spot being smaller than the actual focal spot.
There is one drawback…..the heel effect

## Slide 34: The Heel Effect
The heel effect is due to a portion of the x-ray beam being absorbed by the anode.

## Slide 35: The Heel Effect
******Some news you can use.
Cathode and anode sides of tube housing are labeled near electrical cable attachment.

## Slide 36: X-Ray Generators
The device that supplies electric power to the x-ray tube.
Starts with a source of electrical energy (DUH!)

## Slide 37: X-Ray Generators
An x-ray tube cannot use simple alternating current
An alternating current looks like a sine wave. It goes up and it goes down. First positive, then negative.
If this wave is applied to an x-ray tube electrons would first go toward the anode, then reverse and go toward the cathode.
This would only happen one time because the cathode would be destroyed.
To keep electrons going in one direction, the generator must first convert the alternating current into direct current. A rectifier performs this function.

## Slide 38: X-Ray Generators
A Rectifier is a device that allows
There are three ways to rectify alternating current and make it flow in only one direction

## Slide 39: X-Ray Generators
Half wave rectification
–The negative part of the sine wave is simply chopped off. A generator that produces this type of waveform is called a single phase, half wave rectified generator.
–This type of generator produces 60 pulses of x-rays a second
–X-rays are produced in spurts, like taking a picture with a strobe light. It works but is inefficient.

## Slide 40: X-Ray Generators
Full wave rectification
–The negative part of the sine wave is inverted.
–A generator that produces this waveform is called a
single phase, full wave rectified generator.
–It produces 120 pulses of x-rays each second

## Slide 41: X-Ray Generators
So now we have rectified the current into a form of direct current that can produce x-rays during a whole cycle, but still in a cyclical manner. There are peaks and valleys in the waveform
There is something better – a method that will produce x-rays at a near constant level (that is our goal by the way, to produce x-rays as constantly as possible)

## Slide 42: X-Ray Generators
Three phase, full wave rectified generator
–A generator takes three separate lines of current, that are out of phase, performs a full wave rectification, and superimposes them.
–Tough to describe, so look at the diagram

## Slide 43: X-Ray Generators
This wave is still pulsatile, but more uniform from peak to valley
These are expensive units to purchase, and wiring is also expensive
Uncommon in veterinary offices

## Slide 44: X-Ray Generators
One last Generator, I promise!
The high frequency generator
–Still do the rectifying, but convert the 60HZ current to
produce a whopping 100kHZ output.
–Just know that a high frequency generator can produce a near constant beam of x-rays.

## Slide 45: Quick Review
We want a constant beam of x-rays so we do a bunch of stuff like rectifying the wave, using a three phase current, or increasing the frequency of the output.
What happens if the current coming in from the wall is not constant? You can have the best generator in the world but it can’t do a thing with unstable current coming into the generator. Garbage in, garbage out.

## Slide 46: Line Voltage Compensation
The solution!
A line voltage compensator adjusts the incoming line voltage
Some machines do it automatically, but some (portable units) require it manually. Don’t forget to do it, you will get a crummy underexposed film

## Slide 47: Care of the machine
Do not drop or hit the x-ray tube. It is fragile
Don’t leave your x-ray machine on continuously.
Don’t hold down the rotor button prior to making a radiograph any longer than you have to – the filament is heating during this time and it will shorten its lifespan.
Don’t make too many high KV/MA exposures too rapidly in succession. This overheats the tube.