## Slide 1: Radiation Safety

## Slide 2: RADIATION ORIGINS
Radiation comes from many sources
Manmade and natural
Natural
  Terrestrial
  Cosmic interactions
  Internal our tissues contains radionuclides we ingest or inhale

## Slide 3: RADIATION ORIGINS
Manmade
  We make it
  Products contain radioactive material
  Air travel
  Nuclear weapons, power
  Medical
    Most of manmade comes from

## Slide 4
Put things into perspective
We are exposed naturally
BUT need to protect ourselves because we have increase exposure potential

## Slide 5: What are X-Rays?
X rays are a form of electromagnetic radiation
Arise as electrons are deflected from their original paths
X rays are capable of traveling long distances through air and most other materials
X rays require shielding to reduce their intensity
X rays originate in the electronic shell (remember the electrons around the nucleus)

## Slide 6: Causes of Exposure
Exposure to the Primary Beam
Exposure from secondary scatter radiation caused by interaction of the primary beam with objects in its path
Exposure from ”leakage” radiation from the x-ray tube housing

## Slide 7: Exposure to the Primary Beam
At no time should any part of your body be exposed to the primary beam even if that part of your body is covered by protective clothing

## Slide 8: Exposure due to Scatter Radiation
known as secondary radiation
•

## Slide 9: Exposure due to Scatter Radiation
The amount of scatter is dependent on:

## Slide 10: Exposure due to Scatter Radiation
Scatter is produced in all directions and travels in straight lines.

## Slide 11: Exposure due to Scatter Radiation
Careful collimation, and correct kVp settings will help reduce scatter
Look away from the primary beam to reduce exposure to the lens of the eye
Do not lean over the animal
Always wear lead shielding
Use chemical restraint as necessary
Utilize positioners

## Slide 12: Radiation From X-ray Tube Housing
Current regulations for the manufacturing of x-ray tubes requires sufficient shielding to minimize exposure to personnel and patients
Many veterinary clinics use older equipment with minimal shielding
  If this is of concern, the x-ray tube should be checked by the state department of health

## Slide 13: Radiation Exposure Units
Unit of absorbed dose:
  Gray (Gy)
  Rad

## Slide 14: Radiation Exposure Units
Unit of dose equivalent:
Each type of radiation has a quality factor (QF)
  Reported as Rem (roentgen equivalent man) or Sieverts
  Dose equivalent (rem or Sv)=absorbed dose (Gy or rad)x QF

## Slide 15: ALARA (As Low As Reasonably Achievable)
An ongoing series of decisions about possible radiation protection action
  Eg: using positioning devices or chemical restraint to reduce exposure to personnel
  You should always be thinking about how to reduce your exposure

## Slide 16: Radiation Injury
Radiation damages cells by disrupting vital molecules
Dependent upon

## Slide 17: Radiation Injury
Dependent upon
  Sensitivity of body cells

## Slide 18: Biological Effects of Ionizing Radiation
There are two types of radiation damage
  Somatic
  Genetic

## Slide 19: Biological Effects of Ionizing Radiation
Due to the transfer of energy to the tissue as radiation interacts with the body
There is a localized release of large amounts of energy
The total energy absorbed is important, but not so critical as the size of the individual packets of energy received

## Slide 20: Biological Effects of Ionizing Radiation
Somatic Damage
  Describes damage to the body that may not be apparent for some time but does manifest itself during the recipients lifetime
  Sometimes this damage may never become apparent because the body may repair itself
  Different cell types have different sensitivities and abilities to heal

## Slide 21: Biological Effects of Ionizing Radiation
Genetic Damage:
  Results from injury to the genes (DNA) of reproductive cells
  These injuries do not show up until the damaged individual reproduces and the mutated genes create a child
  Gene mutations

## Slide 22: Radiation Protection – Time
The dose of radiation a worker receives is directly proportional to the amount of time spent in a radiation field.

## Slide 23: Radiation Protection-Distance
Radiation exposure decreases rapidly as the distance between the worker and the X-ray device increases. The decrease in exposure from a point source, such as an X-ray tube, can be calculated by using the inverse square law.

## Slide 24: Inverse Square Law
This law states that the amount of radiation at a given distance from a point source varies inversely with the square of the distance..

## Slide 25
twice the distance from an x-ray tube will reduce the dose to one-fourth of its original value (1/2x2)
increasing the distance by a factor of three will reduce the dose to one-ninth of its original value (1/3x3)
IF you go 10 xs as far away you decrease your dose becomes 1/100th of its original value (1/10x10)

## Slide 26: Inverse Square Law
Maintaining a safe distance, therefore, represents one the simplest and most effective methods for reducing radiation exposure.

## Slide 27: Radiation Protection - Shielding
Radiation exposure to personnel can also be reduced by placing an attenuating material between a worker and the x-ray tube. Thus, substances such as lead, that are very dense and have a high atomic number, are very practical shielding materials because of the abundance of atoms and electrons that can interact with the x-ray photon. Shielding is often incorporated into the equipment, such as the metal lining surrounding the x-ray tube. It may also consist of permanent barriers such as concrete and lead walls, leaded glass, and plastic movable screens.

## Slide 28: Protective Apparel
Perform visual inspections
Perform radiographic inspections
  AAHA requires
Store apparel correctly
  Hang up don’t fold

## Slide 29: How Much is Too Much?
Maximum Permissable Dose (MPD)
  An amount of irradiation that does not involve a risk to the health of radiation workers so great that it significantly influences future generations or the individuals occupationally exposed

## Slide 30: Maximum Permissible Dose (MPD)
Occupationally exposed individuals older than 18, can receive up to 0.05 Sv = 5 rems/year.
Non-occupationally exposed persons can receive 0.001 Sv = 0.1 rem/year.
***No person under 18 may enter a radiographic suite unless ordered by a medical doctor

## Slide 31: Personnel Monitoring Devices
Dosimeters should be worn by personnel at all times during radiographic procedures

## Slide 32: Personnel Monitoring Devices
Types:
  Film Badge- piece of film inside that is developed
  Thermoluminescent dosimeter (TLD)
    crystals absorb radiation when heated emit light , more light = more radiation
  Optically stimulated luminescence
  Pocket ionization chamber
    most complex
    read after each procedure

## Slide 33: Personnel Monitoring Devices
Wear badge up around head/neck area
Care

## Slide 34: Limiting your Exposure
ALARA
Time
Distance
Shielding
Take care of PPD and badges

## Slide 35: Limiting your Exposure
Radiation Safety Rules
  Remove all unnecessary personnel from the radiographic suite
  Never permit persons under the age of 18 or pregnant women in the radiographic suite when in use
  Rotate personnel who assist in radiographic procedures to minimize exposure

## Slide 36: Limiting your Exposure
Radiation Safety Rules
  Use mechanical restraints whenever possible
  Use chemical restraint whenever possible
  Always wear protective apparel
  Wear film badges near the collar outside the lead apron to monitor radiation exposure to the thyroid gland, face, and eyes
  Plan the radiographic procedure carefully to avoid the need for retakes
  Maintain darkroom chemicals in good operating condition
  Have the x-ray machine calibrated annually by a qualified expert

## Slide 37: Limiting your Exposure
Radiation Safety Rules
  Have an adequate technique chart
  Use positioning aids
  Quality control measurements and tests are performed
  Remember that patience is an important virtue!

## Slide 38: Limiting your Exposure
Radiation Safety Rules
  Never permit any part of the body in the primary beam
  Use collimation whenever possible to decrease field size and scatter radiation
  Never handhold the x-ray tube

## Slide 39: Radiation Safety and pregnancy
Fetus particularly susceptible first 4 months
Is it ok to continue taking radiographs?
  Million dollar question with no clear answer
MPD is lower for pregnant women
  What if they need radiographs/CT for their own health reasons?
Probably best to not take radiographs

## Slide 40: Radiation safety and pregnancy
What to do when you find out you are?
Alert your supervisor maybe in writing
Should look at your most recent dosimeter report
If opt to continue to perform radiology