## Slide 1: Film and Film Processing

## Slide 2: In this lecture
Know the composition of radiographic film
Know (basically) how a latent image is formed
Know the steps of development
Understand proper safelight use

## Slide 3: Radiographic Film
Radiographic film consists of two major components
  A Polyester Base that provides support
  Film Emulsion

## Slide 4: Radiographic Film
Film emulsion is composed of two main ingredients:
  Silver Halide Crystals
  Gelatin

## Slide 5: Radiographic film
Emulsion

## Slide 6: Radiographic Film
Different types of radiographic film (there are hundreds) vary in a similar way
The size, shape, composition, and number of particles of silver halide affect the characteristics of the radiographic film

## Slide 7: Radiographic Film
The major effects that altering the emulsion have on film are:
  Film Latitude
  Film Contrast
  Film Speed
  Film Detail
  Light Color (spectral) Sensitivity

## Slide 8: Radiographic Film
Film Latitude
  High latitude means you can mess up pretty bad and still get a decent film, but…
  High latitude has low contrast, and more shades of gray

## Slide 9: Radiographic Film
Film Contrast
  Contrast is a complicated subject, and is affected by many factors other than the film
  Just know that the film you choose will affect the contrast in your final image

## Slide 10: Radiographic Film
Film Speed
  Faster film can be used to make faster exposures
  Results in less patient motion and less exposure to patient and personnel

## Slide 11: Radiographic Film
Film Detail
  Some film will give you exceptional detail and some won’t

## Slide 12: Radiographic Film
Light Color Sensitivity
  Your radiographic film must compliment your screens

## Slide 13: Toward Development
Here goes a quick, concise explanation of how that dull radiographic film acquires and hold an image that we can later process

## Slide 14: Toward Development
Unexposed silver halide within the emulsion are green or purple in color
Metallic silver is black

## Slide 15: Toward Development
The pattern of this conversion parallels the light given off from the screen, which represents the anatomic part you are imaging
“sensitivity speck”
“latent image”

## Slide 16: Toward Development
We cannot see this latent image until it is developed.
When it is developed the entire silver halide crystal containing the sensitivity speck is converted to metallic silver
The remaining, unexposed, silver halide grains are removed during processing

## Slide 17: In the Darkroom
Overall, the process of film development is exactly the same in both manual and automatic processing

## Slide 18: In the Darkroom
There will be problems with development
It is your job to notice, and possibly fix, the processor when it breaks
So it is important to know the following:

## Slide 19: In the Darkroom
Processing is composed of four separate steps
  Development:
  Fixer:

## Slide 20: In the Darkroom
  Wash:
  Drying:

## Slide 21: In the Darkroom
The whole developing process must take place at a specific temperature
This is why you must allow the processor to warm up
It is also why you must be vigilant in monitoring the temperature of your development solution if you are manually processing.

## Slide 22: In the Darkroom
If the temperature is too hot your film will look
If the temperature is too low, it will look
The temperature is monitored and regulated in an automatic processor
With manual processing, you will have to adjust your developing time depending on the temperature of your developing solutions

## Slide 23: In the Darkroom
Automatic processors
  Work at a higher temperature
  Have more concentrated chemicals
  Result faster development than manual

## Slide 24: In the Darkroom
More on manual processing
  Solution replacement: exhausted chemicals are a primary cause of poor quality radiographs
  Chemicals that have lost their potency will produce radiographs that have decreased contrast and density
  In general, chemicals in hand-processing tanks should be changed every 4-6 weeks

## Slide 25: Safelights
Safelights are only safe if used properly
The safelight filter must be matched to the film you use
Using an inappropriate safelight color will fog your film
Also, the safelight must be of the correct wattage
It must be located the correct distance from the tabletop

## Slide 26: Did you know????
90% of all technical errors occur in film processing

## Slide 27: One last thing….
The radiograph is part of the medical record

## Slide 28: One last thing….
You are required by law to record on each radiograph

## Slide 29: One last thing….
Since they are part of the medical record, your practice owns them
You are not required to give them to a client if they request them
Clients pay for the interpretation of the radiograph, not the piece of film itself

## Slide 30: Oh, yeah…
Practical film handling 101
  Treat film well
  It is sensitive to heat, pressure, light, x-rays, moisture, age, and static electricity

## Slide 31: Oh, yeah…
The top 5 ways to properly care for your film are:
  Store boxes of film on end to reduce pressure on the film
  Store film in a cool room (< 70 degress)with low humidity (40-60%) (not on top of the processor)
  Obviously, don’t store it near your x-ray machine where it may be accidentally exposed
  Don’t buy large quantities of film that will expire before you can use it
  When handling film, be gentle placing it in and taking it out of the cassettes

## Slide 32: Hold on, there is more….

## Slide 33: A little more on manual vs automatic processing
And silver recovery.

## Slide 34: Processing Techniques
Manual
  1 hour
Automatic
  90 seconds
  Less variation (standardized)

## Slide 35: Manual Processing
Prep
  Proper temp.
  Stirred
    Don’t share between tanks
  Turn on the safelight
Notes: Fingernails can damage screens and film

## Slide 36: Manual Processing Cont.
Tension clip hanger
  Stationary clips first
  Movable clips second
  Stretch film
Channel hanger
  Hold with one hand and slide the film into the channel with the other

## Slide 37: Manual Processing Cont.
Developing
  Agitate film while in developer to remove air bubbles from film surface
  5 minutes at 68 degrees
  While processing, refill the cassette
    Carfeul to have dry hands when reloaded
    Water spots can cause an artifact

## Slide 38: Manual Processing Cont.
Rinse
  Tilt film so chemical carryover goes into the rinse bath
  This places more of the exhausted developer into rinse
  Agitated in rinse for 30 seconds
Fix
  Agitate film for about 15 seconds to remove air bubbles from film surface
  Fix twice the time of developing example 10 minutes at 68 degrees
  Can view in normal room light after 1 minute but need to place back into fixer

## Slide 39: Manual Processing Cont.
Wash for 20-30 minutes at 68 degrees
Drying
  Dust free environment
  Don’t allow films to touch
  Cut off sharp points on corners where tension clip hangers put holes in corners
Store in envelope

## Slide 40: Automatic Processing
Highly standardized
Produces dry film in short period
Costly machine
  Pays for itself in a short period of time

## Slide 41: Automatic Processing Cont.
Same routine as manual processing
Higher temps and special chemicals
Film transported through the machine with rollers at controlled speed
Rinse between developer and fixer eliminated
  Carryover removed by compression of rollers on film

## Slide 42: Automatic Processing Cont.
Chemicals in peak condition because they are replenished on regular basis
  Tubs under processor
  Maintain temp and mix chemicals
Maintenance
  Solution level check
  Replenishment rate check
  Temp check
  Roller operation check
  Rinsing and wiping of rollers and racks
  Regular cleaning of tanks

## Slide 43: Silver Recovery
Fixer removes the unexposed silver halide crystals from film
  Results in high concentrations of silver in fixer
Silver recovery unit removes the silver

## Slide 44: Silver Recovery
Recycling standard
  Metallic replacement
  Electrolytic recovery
  Chemical precipitation
USA pollution control
  Heavy metals cannot be disposed in septic system
Consider digital machines – no silver to worry about!!
Notes: Fix and and old radiographs should be recycled

## Slide 45: Silver Recovery Cont.
Metallic replacement
  Replaces silver in fixer with another metal
  Glass jar containing steel wool
  Silver fuses to the iron in steel wool
Electrolyte recovery
  2 plates that pass a low electric current
  Negatively charged silver ions attracted to the plates
  Fixer solution can be reused
Notes: Reuse of fix requires much chemical analysis

## Slide 46: Silver Recovery Cont.
Chemical precipitation
  Addition of more chemicals to precipitate silver from fix
  Silver forms a sludge
  Sludge filtered, dried and packed