## Slide 1: Creating a Veterinary Radiographic Technique Chart
Amy Crane, DVM

## Slide 2: Step 1: Get your radiology house in order
Have your processor serviced
Be sure that you are using screens that are all the same age, speed, and manufacturer
Use a dog that weighs about 40 pounds but is not overweight

## Slide 3: Step 2: Select your mAs
In veterinary medicine, patient motion is a great concern
We like to use a high mAs and low kVp technique

## Slide 4: Step 2: Select your mAs cont.
The following are recommended mAs based on a par (medium, 200) speed intensifying screen
–Tabletop (no grid) extremity:
–Thorax:
–Abdomen:
–Spine:
Important to note the difference between the mAs settings in regions!!!!!!!!!!!

## Slide 5: Step 2: Select your mAs cont
If your x-ray machine only has one mA station you just select your mA and pick the speed to give you the desired mAs.
For example: if you have a 300mA station and you wanted to use a 5mAs for a thoracic technique chart you would pick
–300mA x 1/120sec = 2.5mAs (extremity)
–300mA x 1/60sec = 5mAs (thorax)
–300mA x 1/40sec = 7.5mAs (abdomen)
–300mA x 1/30sec = 10mAs (spine)

## Slide 6: Step 2: Select your mAs cont
If your x-ray machine has two mA stations I suggest that for extremity techniques you use the smaller of the mA stations (usually 100mA) and for all other applications you use the larger mA station (usually 300mA). In this case your settings would be as follows:

## Slide 7: Step 2: Select your mAs cont
–100mA x 1/40sec = 2.5mAs (extremity)
–300mA x 1/60sec = 5mAs (thorax)
–300mA x 1/40sec = 7.5mAs (abdomen)
–300mA x 1/30sec = 10mAs (spine)

## Slide 8: Step 2: Select your mAs cont
*****The previous suggestions were for par (medium, 200) speed intensifying screens

## Slide 9: Step 3: Select your initial kVp
This step is to create a “perfect” radiograph
To do that we need to find a kVp to go along with our suggested mAs setting

## Slide 10: Step 3: Select your initial kVp
To pick a starting kVp use Sante’s Rule

## Slide 11: Step 3: Select your initial kVp
If you are using a…..
–5:1 grid add
–8:1 grid add
–12:1 grid add

## Slide 12: Step 3: Select your initial kVp
Most veterinary applications use an 8:1 grid
If you know you are using a grid, but don’t know what kind of grid is under your table assume it is an 8:1 grid
Remember, grids are not used in table top techniques
If you are making a technique chart for a table top study use 0 for the grid factor

## Slide 13: Step 4: Expose the Perfect Film
The goal in this step is to obtain a radiograph with a “perfect” exposure
The technique you use to generate this radiograph will be used to create the rest of the technique chart.
Take your time and make this radiograph as good as it can be
It may take 5 or 6 tries to get it right but the time you spend on this step will be worth it in the end

## Slide 14: Step 4: Expose the Perfect Film
To get started, take a radiograph with the mAs I recommended above for each particular study, and set your kVp according to Sante’s Rule
For example: if I were creating an abdominal technique, using a 40 inch SID, an 8:1 grid, and my dog measures 15cm then I would expose a radiograph at 7.5mAs and 80kVp.
Hopefully, that exposure will be in the ballpark and the radiograph will be fairly well exposed

## Slide 15: Step 4: Expose the Perfect Film
Unfortunately, this is not always the case
  first look at film density

## Slide 16: Step 4: Expose the Perfect Film
Once density is good now time to perfect contrast by changing the kVp

## Slide 17: Step 5: Make the Technique Chart
Now that you have a properly exposed radiograph, you are over the hump and the rest is easy
To create a technique chart simply start with your “perfect exposure” and extrapolate to find the values of kVp for other measurements according to the following rules

## Slide 18: Step 5: Make the Technique Chart
Subtract 2 kVp from the original kVp for each cm decrease from the original measurement
Add 2 kVp to the original kVp for each cm increase from the original measurement up to 80kVp
Add 3 kVp for each cm increase that places the kvp above 80 up to 100
Add 4 kVp for each cm increase that places the kVp above 100

## Slide 19: Step 5: Make the Technique Chart
For example…let’s say that we started with a perfect exposure of 7.5mAs at 80kVp and our patient measured 15cm
We would make an abdominal technique chart as follows

## Slide 20: Step 6: Create a technique chart for each different study as abdomen, thorax, extremity, spine
Repeat the above process to create these additional technique charts

## Slide 21
Also remember every animal is different
fat thin
muscular/dense
puppy/kitten
exotic
so settings (kVp) may need to be changed a little bit need to evaluate every film as it comes out